#	Chip name:	Chip ID:	Flash size, Kb	Flash page/word size, b:	Ram size, Kb	Mac address offset, size:	Info page offset:	Support USB:	Lock data size, bytes:	Lock data place:	Comment:
1.	CC2530	0xA5	32, 64, 128, 256	2048/4	8, 8, 8, 8	0x780C, 8	0x7800 - 0x8000	-	16	Flash	The primary IEEE address resides in info page and is read only. The secondary IEEE address, which is optional, is stored at the end of the flash in the last 8 bytes before the lock bits.
	CC2531	0xB5	128, 256	2048/4	8, 8	0x780C, 8	0x7800 - 0x8000	●
	CC2533	0x95	32, 64, 96	1024/4	4, 4, 6	0x780C, 8	0x7800 - 0x8000	-
	CC2540	0x8D	128, 256	2048/4	8, 8	0x780E, 6	0x7800 - 0x8000	●
	CC2541	0x41	128, 256	2048/4	8, 8	0x780E, 6	0x7800 - 0x8000	-
	CC2543	0x43	18, 32	1024/4	1	-	0x7800 - 0x8000	-
	CC2544	0x44	32	1024/4	2	-	0x7800 - 0x8000	●
	CC2545	0x45	18, 32	1024/4	1	-	0x7800 - 0x8000	-
2.	CC2430	0x85	32, 64, 128	?/4	8, 8, 8, 8	0xDF43, 8	2Kb, special flash	-	1	Info pages	IEEE address is stored in the last 8 bytes of the flash
	CC2431	0x89	32, 64, 128	?/4	8, 8, 8, 8	0xDF43, 8		-
3.	CC2510	0x81	8, 16, 32	?/2	1, 2, 4	-	1Kb, special flash	-	1	Info pages
	CC2511	0x91	8, 16, 32	?/2	1, 2, 4	-		●
4.	CC1110	0x01	8, 16, 32	?/2	1, 2, 4	-	1Kb, special flash	-	1	Info pages
	CC1111	0x11	8, 16, 32	?/2	1, 2, 4	-		●
	CC430										Not supported by CC Debugger
	CC1010										Not supported by CC Debugger